## Slide 1: Low-cost deadlock avoidance in direct interconnection networks
Enrique Vallejo
http://personales.unican.es/vallejoe/
Invited talk
9th International Workshop on
Interconnection Network Architecture:
On-Chip, Multi-Chip (INA-OCMC) 2015

## Slide 2: Index
Introduction
  Direct interconnection network topologies: low radix
  Deadlock avoidance mechanisms
  Topologies proposed for high-radix networks
Dragonfly networks
  Topology and routing
  OFAR: Injection restriction
  RLM: Path restriction
  OLM: Modified Resource-class restriction
Evaluation results
Conclusions

## Slide 3: 1. Introduction 1.1 Direct Interconnection network topologies
Direct topology: no transit routers, all routers have computing nodes directly attached.
Previous trends on direct interconnection network Architectures: Low radix, high diameter
  Hypercubes
  2D/3D Meshes & Tori
    Earth simulator
    Cray: T3D, T3E, XT3-4-5, XK6-7
    BlueGene /L /P
  5D Tori
    BlueGene /Q
    Tofu (K computer)

## Slide 4: 1. Introduction 1.2 Deadlock avoidance mechanisms
HPC interconnection networks are usually lossless & deadlock-free.
The deadlock freedom mechanism employed depends on
  Topology, and
  Routing mechanism
It impacts router design & cost: #VCs, buffer area, allocation, etc.
Deadlock-free routing implemented via restrictions:
  Path restrictions: Cycles never appear on the network
    Dimension-Ordered Routing (DOR)
    Turn model [1], O1Turn [2]
  Resource-class restrictions: Impose a fixed order for VCs
    Distance classes (per-hop increasing order) [3] – relatively high cost!
    Datelines [4]
  Injection restriction: Avoid injecting traffic if it could block the network
    Bubble routing [5,6]
[1] Glass & Ni, “The turn model for adaptive routing”, ISCA’92
[2] Seo et al. “Near optimal worst-case throughput routing for two-dimensional mesh networks”, ISCA’05
[3] Gunther, “Prevention of deadlocks in packet-switched data transport systems,” Trans. Comm’81.
[4] Dally & Seitz, “The Torus Routing Chip”, J. Distributed Computing 1986
[5] Carrión, et al, “A flow control mechanism to avoid message deadlock in k-ary n-cube networks," HiPC’97.
[6] Puente, Izu, Beivide et al, “The Adaptive Bubble Router”, J. PDC’01.

## Slide 5: 1. 2 Deadlock avoidance in low-radix networks Example: multidimensional torus
Dateline: 2 VCs to avoid cycles
Use example: Cray T3E to XT7
4-ary 2-cube
Figure: Dally & Towles, Principles and Practices of Interconnection Networks”, MK 2003

## Slide 6: 1. 2 Deadlock avoidance in low-radix networks Example: multidimensional torus
[5] Carrión, et al, “A flow control mechanism to avoid message deadlock in k-ary n-cube networks," HiPC’97.
[6] Puente, Izu, Beivide et al, “The Adaptive Bubble Router”, J. PDC’01.
Bubble flow control: Halt injection when it could fill buffers and cause deadlock
  Leave at least one slot empty after injection (2 slots required)
  Only for virtual cut-through switching (wormhole variants proposed)
  Used in IBM BlueGene series (/L, /P, /Q)
X
X
X
X
VCT
+
Room (local) for 2 packets
injection queue
or
other dimension

## Slide 7: 1. Introduction 1.3 Direct Interconnection network topologies
Technological trends suggest [7] the use of high-radix routers
  Multiple thin ports rather than few fat ones
High-radix, low diameter direct topologies:
  Flattened butterflies [8]
    Also: HyperX [9],
    based on Hamming graphs
  Dragonflies [10]
    IBM 775 (PERCS [11], Torrent router)
    Cray XC30-40 (Aries router, [12])
  Slimflies [13]
    Maximum density for a given diameter
  …
[7] Kim, Dally, Towles, Gupta, “Microarchitecture of a high-radix router,” ISCA’05
[8] Kim, Dally, Abts, “Flattened butterfly: A cost-efficient topology for high-radix networks”, ISCA’07
[9] Ho Ahn et al, “HyperX: topology, routing, and packaging of efficient large-scale networks”, SC’09
[10] Kim, Dally, Scott, Abts. Technology-Driven, Highly-Scalable Dragonfly Topology. ISCA '08
[11] ] Arimilli et al, “The PERCS high-performance Interconnect”, HOTI’10
[12] Faanes et al, “Cray Cascade: a Scalable HPC System based on a Dragonfly Network,” SC12, [13] Besta & Hoefler, “Slim Fly: A Cost Effective Low-Diameter Network Topology”, SC’14

## Slide 8: Index
Introduction
  Direct interconnection network topologies: low radix
  Deadlock avoidance mechanisms
  Topologies proposed for high-radix networks
Dragonfly networks
  Topology and routing
  OFAR: Injection restriction
  RLM: Path restriction
  OLM: Modified Resource-class restriction
Evaluation results
Conclusions

## Slide 9: 2 Dragonfly networks 2.1 Topology and routing
Differences between a traditional datacenter network and a Dragonfly network
2 main variations:
· Fat-tree: faster links in higher levels
· Folded clos: parallel switches in higher levels
“pod”
Dragonfly
Tree

## Slide 10: 2 Dragonfly netorks 2.1 Topology and routing
[3] K. Gunther, “Prevention of deadlocks in packet-switched data transport systems,” Trans. Communications 1981.
Minimal Routing
  Longest path: 3 hops
    local – global – local
  Deadlock avoidance:
    3 resource classes [3]:
    VC0 - VC1 - VC2
    2 VCs per local port + 1 VC per global port
  Good performance under uniform traffic UN
  Saturation of the global link with adversarial traffic ADV+N
Source group i
Destination group i+N

## Slide 11
2 Dragonfly networks 2.1 Topology and routing
Valiant Routing [10, 14]
  Also “global misrouting”
  Selects a andom intermediate group
  Balances use of links
  Doubles latency
  Halves max. throughput under Uniform traffic
  Longest path 5 hops:
    local – global – local – global – local
  Deadlock avoidance:
    3 VCs per local port + 2 VCs per global port
[10] Kim, Dally, Scott, Abts. Technology-Driven, Highly-Scalable Dragonfly Topology. ISCA '08
[14] L. Valiant, “A scheme for fast parallel communication," SIAM journal on com-
puting, vol. 11, p. 350, 1982.

## Slide 12: 2 Dragonfly networks 2.1 Topology and routing
Adaptive Routing
  Dynamically chooses between minimal and non-minimal routing.
  Relies on the information about the state of the network
  Source routing  Congested global queues can be in other routers
Piggybacking Routing (PB) [15]
  Each router flags if a global queue is congested
  Broadcast information about queues
    Remote information
  Chooses between minimal and Valiant
  Source routing
[15] Jiang, Kim, Dally. Indirect adaptive routing on large scale interconnection networks. ISCA '09. Figure taken from the presentation
Source
Router
Congestion
Busy
Free
Global
MIN
Global
VAL
SOURCE
GROUP
Router
Router

## Slide 13: 2 Dragonfly networks 2.1 Topology and routing – local misrouting
Saturation of local links can also limit performance [15]
  Reduces max. throughput to 1/h. For h=16, Th ≤ 0.0624 phits/c (6,24%)
Occurs with intra-group and inter-group traffic
  Near-Neighbor traffic pattern: A single local link connects source and destination node  Saturation
  Pathological problem when using Valiant routing with adversarial traffic
[16] García et al, et al, “On-the-fly adaptive routing in high-radix hierarchical networks,” ICPP’12

## Slide 14: 2 Dragonfly networks 2.1 Topology and routing – in-transit misrouting
“Local misrouting” avoids saturated local links
  Send packets to a different node within the group (non-minimal local hop), then to the destination (minimal local hop)
Longest path: 8 hops
  local – local – global – local – local – global – local – local
Distance-based deadlock avoidance (PAR-6/2): 6 VCs per local port + 2 VCs per global port
  Protocol-deadlock doubles these requirements (12/4 VCs)
  base mechanism with resource classes, too costly!
Non-minimal local hop
Minimal local hop

## Slide 15: 2 Dragonfly networks 2.2 OFAR: Injection restriction
[16] M. García et al, “On-the-fly adaptive routing in high-radix hierarchical networks,” ICPP’12
[17] M. García et al, “OFAR-CM: Efficient Dragonfly Networks with Simple Congestion Management”, HOTI’13
[18] M. García et al, “On-the-Fly Adaptive Routing for dragonfly interconnection networks”, J. Supercomputing’14
OFAR: On-the-Fly Adaptive Routing [16-18]
Deadlock-free escape subnetwork based on injection restriction (bubble)
Fully adaptive without VCs, but lots of “cons”:
Congestion-prone
Theoretically unbounded path lengths

## Slide 16: 2 Dragonfly networks 2.3 RLM Restricted Local Misrouting - Path restriction
Restricted Local Misrouting (RLM) [19] implements adaptive routing with local misrouting using 3/2 VCs (local/global).
Key idea or RLM:
  Use the same VC index for the 2 local hops in a single group
  Forbid certain 2-hop routes to prevent cyclic dependencies
    Deadlock-free by construction
Works with any flow control mechanism (wormhole included)
  IBM PERCS [11] employs wormhole switching!
RLM restricts path diversity, what reduces max. throughput.
[19] García et al, “Efficient Routing Mechanisms for Dragonfly networks”, ICPP’13
[11] Arimilli et al, “The PERCS high-performance Interconnect”, HOTI’10

## Slide 17: 2 Dragonfly networks 2.3 RLM Restricted Local Misrouting - Path restriction
Implementation based on parity and sign of each link.
  Parity of a link: even(odd) if both nodes have the same (different) parity
  Sign: Positive + if destination index > source index
Allowed 2-hop paths from 5 to 0: 5-2-0 and 5-4-0 (odd-, even-) 5-6-0 (odd+, even-)
even-, odd-
[19] García et al, “Efficient Routing Mechanisms for Dragonfly networks”, ICPP’13

## Slide 18: 2.4. OLM: Opportunistic Local Misrouting Modified resource-class restriction
Oppportunistic Local Misrouting (OLM): Routing mechanism using 3/2 VCs with a modified distance-based deadlock avoidance mechanism:
  Minimal routing and global misrouting  Increase VC index
  Local misrouting (opportunistic)  Reuse or decrease VC index
Deadlock freedom: Local misrouting is opportunistic: if the packet cannot advance, there is always a safe “escape” path to the destination using increasing order of VCs: the one without local misrouting
Why it does work? The “safe path” always exists, due to the topology of the network
  Decreasing the index on a local misrouting guarantees that a path with increasing order in the VC index exists, since all routers (but one) in a group have the same distance to the destination group.
[19] García et al, “Efficient Routing Mechanisms for Dragonfly networks”, ICPP’13

## Slide 19: 2.4. OLM: Opportunistic Local Misrouting Modified resource-class restriction
VC indexes: VC1 – VC2 – VC3 – VC4 – VC5
VC1
VC2
VC3
VC1
VC2
VC3
VC4
VC5
Minimal routing
1
2
3
Global misrouting
1
2
3
4
5
VC1
OLM
1
2
1
1
3
4
5
VC2
VC1
VC3
VC4
Source group
Destination group
Interm. group
[19] García et al, “Efficient Routing Mechanisms for Dragonfly networks”, ICPP’13

## Slide 20: 2. Dragonfly networks Deadlock avoidance mechanisms comparison chart
 | Piggy- backing[15] | OFAR [16] | PAR-6/2 [19] | RLM [19] | OLM [19]
Local misrouting |  |  |  |  | 
Congestion-prone (escape network) | NO | YES | NO | NO | NO
VCs in local ports (cost) | 3 | Any | 6 | 3 | 3
Routing freedom In local misrout. | None | Max. | Max | Just Enough | Max
Wormhole support |  |  |  |  | 
[15] Jiang, Kim, Dally. Indirect adaptive routing on large scale interconnection networks. ISCA '09.
[16] M. García et al, “On-the-fly adaptive routing in high-radix hierarchical networks,” ICPP’12.
[19] García et al, “Efficient Routing Mechanisms for Dragonfly networks”, ICPP’13

## Slide 21: Index
Introduction
  Direct interconnection network topologies: low radix
  Deadlock avoidance mechanisms
  Topologies proposed for high-radix networks
Dragonfly networks
  Topology and routing
  OFAR: Injection restriction
  RLM: Path restriction
  OLM: Modified Resource-class restriction
Evaluation results
Conclusions

## Slide 22: 3. Evaluation 3.1 Simulation parameters
Simulated network:
  2.064 routers with 31 ports/router
  129 groups of 16 routers each, 16x8=128 comp. nodes per group
  16.512 servers in the system
FOGSim [20] used with a simple configuration:
  Input-FIFO router model
  Virtual cut-through switching
  No speedup, single-cycle router
  Synthetic traffic: uniform or worst-case patterns
Link latencies and queue sizes:
  10 cycles in local links, 32 phits per VC
  100 cycles in global links, 256 phits per VC
[20] FOGSim Simulator: https://code.google.com/p/fogsim/

## Slide 23: 3. Evaluation 3.2. Latency and throughput
Performance – uniform traffic

## Slide 24: 3. Evaluation 3.2. Latency and throughput
Performance – adversarial ADV+6 traffic

## Slide 25: 3. Evaluation 3.2. Variable local & global misrouting
Intra-group adversarial traffic
Inter-group adversarial traffic

## Slide 26: Index
Introduction
  Direct interconnection network topologies: low radix
  Deadlock avoidance mechanisms
  Topologies proposed for high-radix networks
Dragonfly networks
  Topology and routing
  OFAR: Injection restriction
  RLM: Path restriction
  OLM: Modified Resource-class restriction
Evaluation results
Conclusions

## Slide 27: 4. Conclusions
High-radix networks are cost and energy efficient
  New opportunities & challenges for deadlock avoidance
Their low diameter make distance-based deadlock avoidance mechanism appealing
  But misrouting & protocol deadlock quadruple implementation cost
We have explored alternative low-cost deadlock avoidance mechanisms based on:
  Injection restriction: OFAR
  Path restriction for local misrouting: RLM
  Modified distance-based restriction for local misrouting: OLM
Opportunistic Local Misrouting is competitive with distance-based mechanisms at half the VCs
  And RLM is the best option for wormhole networks
We continue exploring alternative solutions:
  Deadlock avoidance mechanism completeley based on path restrictions (i.e., no VCs required) to be presented on Wednesday [21]
[21] Camarero, Vallejo & Beivide “Topological Characterization of Hamming and Dragonfly Networks and its Implications on Routing”. HiPEAC’15 (WEDNESDAY MORNING!)

## Slide 28: Acknowledgements
Most of our contributions presented here have been developed in the Computer Architecture group from the University of Cantabria, led by Prof. Ramón Beivide
Additional contributors to the results in this presentation include:
  Ramón Beivide (UC)
  Marina García (UC)
  Pablo Fuentes (UC)
  Miguel Odriozola (UC)
  Cristóbal Camarero (UC)
  Germán Rodríguez (IBM Research Zurich)
  Cyriel Minkenberg (IBM Research Zurich)
  Mateo Valero (UPC & BSC)
  Jesús Labarta (UPC & BSC)

## Slide 29: Sources & References
Dally & Towles, “Principles and Practices of Interconnection Networks”, MK 2003
Pinkston, “Deadlock Characterization and Resolution in Interconnection Networks. Marcel Dekker Ed. 2005
[1] Glass & Ni, “The turn model for adaptive routing”, ISCA’92
[2] Seo et al. “Near optimal worst-case throughput routing for two-dimensional mesh networks”, ISCA’05
[3] Gunther, “Prevention of deadlocks in packet-switched data transport systems,” Trans. Comm’81.
[4] Dally & Seitz, “The Torus Routing Chip”, J. Distributed Computing, 1986
[5] Carrión, et al, “A flow control mechanism to avoid message deadlock in k-ary n-cube networks," HiPC’97.
[6] Puente, Izu, Beivide et al, “The Adaptive Bubble Router”, J. PDC’01.
[7] Kim, Dally, Towles & Gupta, “Microarchitecture of a high-radix router,” ISCA’05
[8] Kim, Dally & Abts, “Flattened butterfly: A cost-efficient topology for high-radix networks”, ISCA’07
[9] Ho Ahn et al, “HyperX: topology, routing, and packaging of efficient large-scale networks”, SC’09
[10] Kim, Dally, Scott, Abts. Technology-Driven, Highly-Scalable Dragonfly Topology. ISCA '08
[11] Arimilli et al, “The PERCS high-performance Interconnect”, HOTI’10
[12] Faanes et al, “Cray Cascade: a Scalable HPC System based on a Dragonfly Network,” SC12,
[13] Besta &Hoefler, “Slim Fly: A Cost Effective Low-Diameter Network Topology”, SC’14
[14] Valiant, “A scheme for fast parallel communication," SIAM journal on computing, vol. 11, p. 350, 1982.
[15] Jiang, Kim & Dally. “Indirect adaptive routing on large scale interconnection networks.” ISCA '09.
[16] García et al, et al, “On-the-fly adaptive routing in high-radix hierarchical networks,” ICPP’12
[17] García et al, “OFAR-CM: Efficient Dragonfly Networks with Simple Congestion Management”, HOTI’13
[18] García et al, “On-the-Fly Adaptive Routing for dragonfly interconnection networks”, J. Supercomputing’14
[19] García et al, “Efficient Routing Mechanisms for Dragonfly networks”, ICPP’13
[20] FOGSim Simulator: https://code.google.com/p/fogsim/
[21] Camarero, Vallejo & Beivide “ Topologycal characterization of Hamming and Dragonflies and its implications on routing”. HiPEAC’15 (WEDNESDAY MORNING!)

## Slide 30: Low-cost deadlock avoidance in direct interconnection networks
Enrique Vallejo
http://personales.unican.es/vallejoe/
Invited talk
9th International Workshop on
Interconnection Network Architecture:
On-Chip, Multi-Chip (INA-OCMC) 2015